Congratulations on your purchase of a Cloak Audio Jackdaw 

The Cloak Audio Jackdaw is a unique fuzz pedal. Combining two synthy-sounding octave fuzzes run in parallel - an upper and lower octave fuzz - it covers the whole frequency range. It's dirty and snarly on the low notes, almost like a malfunctioning analogue synth, and relentlessly precise on the higher notes. It is always rewardingly noisy! These parallel fuzzes are mixed together and fed into a filter circuit, the characteristics of which can be changed from a regular tone control to fixed-wah to an envelope-following, more vocal sounding filter.

Operating

Connect a lead from your guitar to the input jack. Connect a lead from the output jack to your amplifier. Make sure a 9V DC centre negative adapter is connected to the power socket.

Controls

Fuzztone: 
Mixes two parallel octave fuzz circuits. The bass fuzz to the left, treble to the right.

Freq: 
Depending where the freq/tone switch is set, this changes the frequency of the tone control or fixed-wah filter.

Volume: 
Sets the master volume of the effect

Blend: 
Blends your guitar’s clean signal with the fuzz effect (fully anticlockwise is clean, fully clockwise is all fuzz)

Sens: 
Sets the sensitivity of the envelope effect. This is active when the Env on switch is down. The red LED about this knob flashes on when the envelope effect is triggered.

Freq/tone switch: 
Chooses between a fixed wah (freq) and more conventional tone circuit.

Env on switch: 
Turns on the envelope effect, which makes a more vocal filter sound depending on how hard you play the guitar. This operates in the frequency range between the freq control setting and the maximum frequency – so if the freq control is fully anticlockwise the envelope effect operates in the whole frequency range.

Tech Specs

The Jackdaw uses true bypass switching

Size: 170 X 90 X 70 mm
Weight: 500 grams 
Power:  9V DC centre negative adapter (2.1mm)
Current draw: 40ma

For powering the pedal, the use of a well regulated power 9V DC power supply is recommended. Batteries aren’t good for the environment. If you always use an external adapter to power the pedal it is recommended that the battery be removed. The use of power supplies other than the type specified may damage the pedal. Never use AC power adapters or exceed 9V DC.

For all support queries, please email Tim at Cloak Audio at timhulio@gmail.com

Happy stomping!